## Slide 1: Sound Generator

## Slide 2: First Cut
Square Wave at fixed frequency
  Middle C is 261.6265 Hz
  50,000,000 MHz / 261.6265 Hz = 191,112.13
  2^18 is 262,144
  Use an 18-bit counter
    Preload to 262,144 – 191,112 = 72032
      0x11578 = 1 0001 0101 0111 1000
    Count up to Terminal Count
    Use Most Significant bit as output
      Not symmetric, but “OK” for easy

## Slide 3: Second Cut
Use same long counter chain
Don’t do a pre-load (do full range count)
Use mux to select counter output bits
Control select mux with register from CPU
Only allows 2X frequencies
  50,000,000 MHz / 262,144 = 190.7 Hz
  2x = 381.4 Hz, 4X = 762.9 Hz, 8X = 1,525.h Hz

## Slide 4: Second Cut (cont’d)
Sounds on keyboards
  190.7 Hz = ~ G3
  381.4 Hz = ~ G4 (above middle C)
  762.9 Hz = ~ G5 (next up)
  1,525.h Hz = ~ G6 (next up)

## Slide 5: Second Cut (cont’d)
18-bit
Counter
4:1
Mux
50 MHz
Clock
Toggle
F-F
Data
Latch
Buzzer
CPU
8
8
4

## Slide 6: Third Cut
Use counter
Load counter with starting value
Count from the value to terminal count
Toggle the output every time terminal count is reached

## Slide 7: Second Cut (cont’d)
Loadable counter entity
  entity counterLoadable is
  port(
  clock: in std_logic;
  clear: in std_logic;
  loadVal: in std_logic_vector(7 downto 0);
  soundOut: out std_logic;
  Q: out std_logic_vector(18 downto 0)
  );
  end counterLoadable;

## Slide 8: Third Cut
Use DDS to generate precise frequencies
50,000,000 Hz clock is 20 nS accuracy
12 notes per octave on a piano
Every octave doubles the frequency

## Slide 9: Third Cut (cont’d)

## Slide 10: Improving “Fidelity”
Square waves are very harsh
Rising/falling edges have a lot of harmonics
Need to soften the edges or make the steps smaller
Smaller steps with the buzzer reduce the volume

## Slide 11: Smoothing the edges
No real options on the card for smoothing the sharp edges
Reduce drive current from 8 mA?
Buzzer has 100 ohm series resistor
Buzzer impedance is TBD

## Slide 12: Characterizing the Buzzer
Buzzers are very small tweeters
OK at high frequencies but still low volume
Very poor at low frequencies
Volume vs frequency curve

## Slide 13: External Solutions?
I/O connector limitation
  All 26-pins are either VGA digital, PS/2 or Power/Ground connections
  Overcoming limitations
    Could steal lower video bits
    Sound with slightly disturb video
    Green has 6 bits
    Steal least significant bit from Red, Green and Blue
    Won’t affect video noticeably in the 2:2:2 Retro-computer case

## Slide 14: 3-bit D/A
Digitize sine wave
Counter start/stop count