## Slide 1
VHDL Sound Generator

## Slide 2
First Cut
Single Tone
Ex:
  16-bit counter
  Clocked at 50 MHz
  MSB = 50,000,000 / 2^16 = 762.93 Hz
  Symmetric waveform since there’s a full count
Code: Counter16Bit.vhd

## Slide 3
First Cut (cont’d)
16-bit
Up
Counter
50 MHz
Clock
CLK50
MSB
Sound Out
to Buzzer
Notes: 1

## Slide 4
First Cut (cont’d)

## Slide 5
First Cut (cont’d)
Expected 763 Hz
Measured 764 Hz (with cursors)
A lot of over/undershoot @ buzzer pin
Limitations
  No mute control
  Fixed Frequency
  Square Wave sounds really annoying

## Slide 6
In pin list at top of Microprocessor entity
BUZZER : out std_logic;
Assign BUZZER to Pin 85 in the Pin Planner
In the architecture of Microprocessor
buzzCounter: entity work.Counter16Bit
port map(
clock => clk,
Q => BUZZER
);
First Cut (cont’d)

## Slide 7
Create Counter16.vhd file and include in project
entity Counter16Bit is
port(
clock: in std_logic; – 50 MHz clock
Q: out std_logic – Most Signif Bit of counter
);
end Counter16Bit;
architecture behv of Counter16Bit is
signal Pre_Q: std_logic_vector(15 downto 0);
begin
process(clock, Pre_Q)
begin
if rising_edge(clock) then
Pre_Q <= Pre_Q + 1;
end if;
end process;
Q <= Pre_Q(15); – MSB of counter goes out
end behv;
First Cut (cont’d)

## Slide 8
First Cut (cont’d)
Add mute control
Use extra bit in the 8 bit register that controls the LEDs
  Use D4 bit of register (D0-D3 are LEDs)
  Register bit is low at power up
  Mute sound when low
  Turn on sound with POKE 65492,16 (6502/6809) or OUT 132,16 (Z80)

## Slide 9
First Cut (cont’d)
Add signal signal buzz : std_logic;
Change entity callout in Microprocessor buzzCounter: entity work.Counter16Bit port map( clock => clk, Q => buzz – Changed to signal ); Add control BUZZER <= buzz and latchedBits(4);

## Slide 10
First Cut
Result
  Single tone
  Mutable
  Accurate (got the frequency expected)
Good Start!

## Slide 11
Second Cut
Improvements
  Add 2 extra counter bits (18-bit counter)
    Route out three counter bits (Q17 downto Q15)
  Add counter taps
    Select tap with remaining control register bits (D5-D7)
    This will give us 3 tones
    Select Q15, Q14, Q13
    Expect frequencies of 248, 496, and 792

## Slide 12
Second Cut
POKE 65492,48 (16 to turn on, 32 for tone)
POKE 65492,80 (16 to turn on, 64 for tone)
POKE 65492,144 (16 to turn on, 128 for tone)
POKE 65492,0 (to turn off)

## Slide 13
Second Cut w/ Taps (cont’d)
18-bit
Up
Counter
50 MHz
Clock
CLK50
MSB
Sound Out
to Buzzer
N bits
Control
Register
CPU
8
8
8
AND-OR
Gates
Notes: <number>

## Slide 14
Second Cut
In Microprocessor entity
buzzCounter: entity work.Counter16Bit
port map(
clock => clk,
selectTap => latchedBits(7 downto 5),
Q => buzz
);

## Slide 15
Second Cut
In Counter18Bit entity
entity Counter18Bit is
port(
clock: in std_logic; -- 50 MHz clock
selectTap: in std_logic_vector(2 downto 0);
Q: out std_logic -- Most Signif Bit of counter
);
end Counter18Bit;
-- concurrent assignment statement
Q <= ((Pre_Q(15) and selectTap(2)) or (Pre_Q(16) and selectTap(1)) or (Pre_Q(17) and selectTap(0)));

## Slide 16
Second Cut (Cont’d)
Limitations
  Binary counter every bit is ½ or 2x the previous bit
    This is one octave
    Steps very small at low frequencies
    Steps very big at higher frequencies

## Slide 17
Third Cut
Square Wave output
Fixed frequency
  Middle C is 261.6265 Hz
  50,000,000 clks/sec / 261.6265 Hz = 191,112.13 clocks
  Next bit up - 2^18 = 262,144
  Use an 18-bit counter
    Starting count = 262,144 – 191,112 = 72032
      0x11578 = 1 0001 0101 0111 1000
    Count up to Terminal Count and then reload
  Use Most Significant Counter bit as sound out

## Slide 18
Third Cut (cont’d)
18-bit
Up
Counter
50 MHz
Clock
18
Compar-
ator
All 1’s
TC
LOAD
1xx..xx
Starting Count
CLK50
MSB
Sound Out
to Buzzer
Notes: <number>

## Slide 19
Second Cut (Cont’d)
Using Most Significant Bit as output is asymmetric
  MSB symmetry is (131072-74032)/262,144 = 22% low/78% high
  Desirable is 50%/50% symmetry
Get symmetry by putting a Toggle Flip Flop on the Terminal Count
  Requires a bit for FF, but one less counter bit

## Slide 20
Sending Output to I/O Pin
Using a LSB of the VGA output for testing
These FPGA retrocomputers use 2:2:2 (R:G:B) outputs to resistor networks
Lowest bit shouldn’t be “missed” in this application

## Slide 21
Third Cut
Use same long counter chain
Don’t do a pre-load (do full range count)
Use mux to select counter output bits
Control select mux with register from CPU
Only allows 2X frequencies
  50,000,000 MHz / 262,144 = 190.7 Hz
  2x = 381.4 Hz, 4X = 762.9 Hz, 8X = 1,525.h Hz

## Slide 22
Third Cut (cont’d)
Sounds on keyboards
  190.7 Hz = ~ G3
  381.4 Hz = ~ G4 (above middle C)
  762.9 Hz = ~ G5 (next up)
  1,525.h Hz = ~ G6 (next up)

## Slide 23
Third Cut (cont’d)
18-bit
Counter
4:1
Mux
50 MHz
Clock
Toggle
F-F
Data
Latch
Buzzer
CPU
8
8
4

## Slide 24
Fourth Cut
Use counter
Load counter with starting value
Count from the value to terminal count
Toggle the output every time terminal count is reached

## Slide 25
Fourth Cut (cont’d)
Loadable counter entity
entity counterLoadable is
port(
clock: in std_logic;
clear: in std_logic;
loadVal: in std_logic_vector(7 downto 0);
soundOut: out std_logic;
Q: out std_logic_vector(18 downto 0)
);
end counterLoadable;

## Slide 26
Fourth Cut
Use DDS to generate precise frequencies
50,000,000 Hz clock is 20 nS accuracy
12 notes per octave on a piano
Every octave doubles the frequency

## Slide 27
Fourth Cut (cont’d)

## Slide 28
Improving “Fidelity”
Square waves are very harsh
Rising/falling edges have a lot of harmonics
Need to soften the edges or make the steps smaller
Smaller steps with the buzzer reduce the volume

## Slide 29
Smoothing the edges
No real options on the card for smoothing the sharp edges
Reduce drive current from 8 mA?
Buzzer has 100 ohm series resistor
Buzzer impedance is TBD

## Slide 30
Characterizing the Buzzer
Buzzers are very small tweeters
OK at high frequencies but still low volume
Very poor at low frequencies
Volume vs frequency curve

## Slide 31
External Solutions?
I/O connector limitation
  All 26-pins are either VGA digital, PS/2 or Power/Ground connections
  Overcoming limitations
    Could steal lower video bits
    Sound with slightly disturb video
    Green has 6 bits
    Steal least significant bit from Red, Green and Blue
    Won’t affect video noticeably in the 2:2:2 Retro-computer case

## Slide 32
3-bit D/A
Digitize sine wave
Counter start/stop count